TSS BULLET RESISTANT ARCHED WINDOW SYSTEM

PART 1 GENERAL

  - REFERENCE

- Underwriters Laboratory UL 752-Standard for Bullet Resisting Equipment & ASTM E119-98- Standard Test Methods for Fire Tests of Building Construction and Materials, NIJ Standard 0108.01-(National Institute of Justice) Standard for Ballistic Resistant Protective Materials, ASTM B 209/B 209M- Standard Specification for Aluminum and Aluminum Alloy Sheet and Plate, ASTM A 666-Standard Specification for Annealed or Cold-Worked Austenitic Stainless Steel Sheet, Strip, Plate and Flat Bar..

  - SUBMITTALS

- The following shall be submitted by the manufacturer in accordance with Sections 13070 and any Special Contract Requirements and coordinate with Sections 01340: Submit for approval prior to fabrication: samples, product data (including preparation, storage and installation methods), cuts & anchor spacing, reinforcement & location , product specifications, shop drawings, test reports (current UL Listing Verification & UL 752 Test Results as provided by Underwriters Laboratories), and printed data in sufficient detail to indicate compliance with the contract documents.

- Manufacturer’s Instructions for installation and cleaning of TSS Bullet Transaction Window Assemblies. All required submittals shall be approved prior to installation.

  - DESIGN PERFORMANCE

- Through the design, manufacturing techniques and material application the TSS Bullet Resistant Arched Window System shall be of the “non-ricochet” type. This assembly shall provide multiple transaction positions utilizing the “Arched Window” configuration.  This design shall employ arched windows in teller line ballistic glazing to complete the “Arched” design.  Each transaction position shall have a stainless steel dip tray as shown on the drawings. Components must be manufactured in strict accordance with the specifications, design and details. All vision panels shall be cut to size with all exposed edges polished.  Necessary holes shall be pre drilled and tapped where required.  Stainless Steel assembly screws and acrylic spacers shall be provided. Frame and channel shall be provided. Anchoring screws shall be provided.

- No field alterations to the construction of the assembly fabricated under the acceptable standards shall be allowed unless approved by the manufacturer and the architect.  Standard manufacturing tolerances shall be +/- 1/16".

- Materials shall meet or exceed UL 752 requirements.

  - QUALITY ASSURANCE

- Manufacturer shall be a Company that specializes in manufacturing products of the specified type with a minimum of five years experience.  Installer shall be a Company that specializes in product type specified and Certified for the installation by the manufacturer.  Manufacturer shall provide a sampling, if required, for evaluation of surface preparation and application workmanship and color/finish to the Architect for approval prior to start of work.

  - DELIVERY, STORAGE & HANDLING

- Delivery of the materials to the project with the manufacturer’s UL Listed Labels intact and legible.  Handle the materials with care to prevent damage.   Store materials inside and under cover, stack flat and off floor. Project conditions (temperature, humidity, and ventilation) shall be within the maximum limit recommendations set by manufacturer.  Do not install products that are under conditions outside these limits.

  - WARRANTY

- All materials shall be warranted against defects for a period of 1 year for the date of receipt at the project site.  .  Certificates of manufacturer’s standard limited warranty shall be provided at project completion.

PART 2 PRODUCTS

2.1ACCEPTABLE MANUFACTURERS

A. Products shall be manufactured by: Total Security Solutions, Inc., 170 National Park Drive, Fowlerville, MI 48836, 800-513-1468. Attn: Sales Department, sales@tssbulletproof.com. Web: www.tssbulletproof.com. No substitutions shall be accepted.

2.2 BULLET RESISTANT ARCH WINDOW SYSTEM

A. Product shall be: TSS Arched Window System:  The Arch System consists of custom prefabricated bullet

resistant wall section panels with secure air passage through the arched window transaction point as required for voice transmission.    Aluminum channel, acrylic mounting clips, acrylic buttresses and accessories for installation are included. Available finishes include clear anodized or powder coated.

- Glazing shall be ______________ (specify options below) as shown on the drawings.

All acrylic pieces shall meet or exceed UL 752 testing for ballistic integrity.  All edges of acrylic shall be filed, sanded after cutting to remove rough edges and then polished until “water clear” transparent.  All through holes for fasteners shall be 3/8” in diameter and be drilled clean.  Chipped edges at through-hole exit points are not acceptable.  All acrylic pieces shall be supported in the proper glazing channel designed for this purpose (see aluminum, Section D).

### Bullet-Resisting Glazing Material Options:

Bullet Resistant Level 1
3/4" LP 750 Laminated
3/4" GCP 750 Glass Clad
1 1/4" Uncoated Acrylic
1 1/4" AR Coated Acrylic

Bullet Resistant Level 2
1" LP 1000 Laminated
1 3/8” Uncoated Acrylic
1 3/8" AR Coated Acrylic
1.05” TSS-002 L/S Glass Clad

Bullet Resistant Level 3
1 1/4" LP 1250 Laminated
1 1/4” TSS-003 L/S Glass Clad

Bullet Resistant Level 4, 5, & 8
TSS-004 L/S, TSS-005 L/S, & TSS-008 L/S

- Cash tray: Brushed Stainless Steel Counter Mounted or Recessed.

1)  Cash tray to be 18 ga. stainless steel, # 4 finish, and 16" x 10" from the outside edge of flanges with a clear opening.

- Aluminum sections to be manufactured in accordance with ASTM B209, Extruded aluminum alloy 6063 T5 Anodized to match the existing décor and be free of sharp edges or burrs when in place.  Glazing Channel: U-Channel specifically designed for securing transparencies tightly in place.  Angles and stops are only acceptable for top attachment.  All exposed aluminum edges shall be clean cut and have no burrs.  Exposed corners shall be rounded and sanded. 

        1)  Frame to be clear or dark bronze anodized aluminum. The bottom of the glazing to be capped with
             corresponding material on the frame.

- Mounting plates and or connecting clips shall be fabricated from 1/8” thick clear polycarbonate.

- Product shall be: TSS Arched Window System.

PART 3 EXECUTION

3.1 PREPARATION

A. Prior to installing the bullet resistive material, the contractor shall verify that all supports have been installed as required by the contract documents and architectural drawings, and approved shop/CAD drawings, if required.  Installer shall notify architect of any unsatisfactory preparation that is responsibility of another installer.

B. Clean and prepare all surfaces per manufacturers recommendations for achieving the best results for the substrate under the project conditions.

3.2 INSTALLATION

A. Do not begin installation until openings have been verified and surfaces properly prepared in accordance with Drawings.  Install in accordance with manufacturer’s instructions and UL 752. Set all equipment plumb.  All products shall be installed per installation instructions provided by Total Security Solutions, if warranty is to be issued.

B. TSS Arched Window System: shall arrive on site completely pre-fabricated to supplied field dimensions. Unit shall be installed in provided opening and secured to structure.

3.3 POST APPLICATION

A. TSS Arched Window System: shall be installed in accordance with manufacturer’s printed recommendations, including adhering to anchoring and finishing details.

B. Inspection and Cleaning: Verify installation is complete and complies with manufacturer’s requirements. Clean product and accessories, removing excess sealant, labels and protective covers.

C. Touch-up, repair or replace damaged products before Substantial Completion.

D. Product Warranty: Applicable warranty shall be issued to owner upon final release of completed project.

**end of section**